## Slide 1: HPC networks: Infiniband

## Slide 2: IBA
The InfiniBand Architecture (IBA) is an industry-standard architecture for server I/O and inter-server communication.
  Developed by InfiniBand Trade Association (IBTA).
It defines a switch-based, point-to-point interconnection network that enables
  High-speed
  Low-latency
  communication between connected devices.

## Slide 3: Infiniband used RDMA based Communication

## Slide 4
Infiniband architecture overview

## Slide 5: Architecture Layers

## Slide 6: InfiniBand VS. Ethernet
 | Ethernet | InfiniBand
Commonly used in what kinds of network | Local area network(LAN) or wide area network(WAN) | Interprocess communication (IPC) network
Transmission medium | Copper/optical | Copper/optical
Bandwidth | 1Gb/10Gb | 2.5Gb~120Gb
Latency | High | Low
Popularity | High | Low
Cost | Low | High

## Slide 7: InfiniBand Devices

## Slide 8: IBA Subnet

## Slide 9: Endnodes
IBA endnodes are the ultimate sources and sinks of communication in IBA.
  They may be host systems or devices.
    Ex. network adapters, storage subsystems, etc.

## Slide 10: Links
IBA links are bidirectional point-to-point communication channels, and may be either copper and optical fibre.
  The base signalling rate on all links is 2.5 Gbaud.
    Link widths are 1X, 4X, and 12X.

## Slide 11: Channel Adapter
Channel Adapter (CA) is the interface between an endnode and a link
There are two types of channel adapters
  Host channel adapter(HCA)
    For inter-server communication
    Has a collection of features that are defined to be available to host programs, defined by verbs
  Target channel adapter(TCA)
    For server IO communication
    No defined software interface

## Slide 12: Addressing
LIDs
  Local Identifiers, 16 bits
  Used within a subnet by switch for routing
  Dynamically assigned at runtime
GUIDs
  Global Unique Identifier
  Assigned by vendor (just like a MAC address)
  64 EUI-64 IEEE-defined identifiers for elements in a subnet
GIDs
  Global IDs, 128 bits (same format as IPv6)
  Used for routing across subnets

## Slide 13: GID: Routing across subnets

## Slide 14: Switches
IBA switches route messages from their source to their destination based on routing tables
  Configured explicitly by Subnet Manager
Switch size denotes the number of ports
  The maximum switch size supported is one with 256 ports
The addressing used by switched
  Local Identifiers, or LIDs allows 48K endnodes on a single subnet
  A 64K LID address space is reserved for multicast addresses
  Routing between different subnets is done on the basis of a Global Identifier (GID) that is 128 bits long

## Slide 15: Management Basics

## Slide 16: Subnet Manager

## Slide 17: Subnet Management
Subnet Manager:
  External software service running on an endhost or switch
  OpenSM – most commonly used
  Assigns Addresses to endhosts and switches
  Directly configures routing tables in each switch and device

## Slide 18: Management Datagrams
All management is performed in-band, using Management Datagrams (MADs).
  MADs are unreliable datagrams with 256 bytes of data (minimum MTU).
Subnet Management Packets (SMP) is special MADs for subnet management.
  Only packets allowed on virtual lane 15 (VL15).
  Always sent and receive on Queue Pair 0 of each port

## Slide 19: Infiniband routing

## Slide 20: Infiniband Routing

## Slide 21: Infiniband Packet Format
GRH: Global Routing Header
  Routes between subnets
BTH: Base Transport Header
  Processed by endnodes
ICRC: Invariant CRC
  CRC over fields that don’t change
VCRC: Variant CRC
  CRC over fields that can change

## Slide 22: Communication Service Types

## Slide 23: Data Rate
Effective theoretical throughput

## Slide 24: Queue-Based Model
Channel adapters communicate using Work Queues of three types:
  Queue Pair(QP) consists of
    Send queue
    Receive queue
  Work Queue Request (WQR) contains the communication instruction
    It would be submitted to QP.
  Completion Queues (CQs) use Completion Queue Entries (CQEs) to report the completion of the communication

## Slide 25: Queue-Based Mode

## Slide 26: Access Model for InfiniBand
Privileged Access
  OS involved
  Resource management and memory management
    Open HCA, create queue-pairs, register memory, etc.
Direct Access
  Can be done directly in user space (OS-bypass)
  Queue-pair access
    Post send/receive/RDMA descriptors.
  CQ polling

## Slide 27: Access Model for InfiniBand
Queue pair access has two phases
  Initialization (privileged access)
    Map doorbell page (User Access Region)
    Allocate and register QP buffers
    Create QP
  Communication (direct access)
    Put WQR in QP buffer.
    Write to doorbell page.
      Notify channel adapter to work

## Slide 28: Access Model for InfiniBand
CQ Polling has two phases
  Initialization (privileged access)
    Allocate and register CQ buffer
    Create CQ
  Communication steps (direct access)
    Poll on CQ buffer for new completion entry

## Slide 29: Memory Model
Control of memory access by and through an HCA is provided by three objects
  Memory regions
    Provide the basic mapping required to operate with virtual address
    Have R_key for remote HCA to access system memory and L_key for local HCA to access local memory.
  Memory windows
    Specify a contiguous virtual memory segment with byte granularity
  Protection domains
    Attach QPs to memory regions and windows

## Slide 30
InfiniBand creates a channel directly connecting an application in its virtual address space to an application in another virtual address space.
The two applications can be in disjoint physical address spaces – hosted by different servers.

## Slide 31: Communication Semantics
Two types of communication semantics
  Channel semantics
    With traditional send/receive operations.
  Memory semantics
    With RDMA operations.

## Slide 32: Send and Receive
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
Fabric
WQE

## Slide 33: Send and Receive
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
WQE
Fabric
WQE

## Slide 34: Send and Receive
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
WQE
Remote Process
Process
Fabric
WQE
Data packet

## Slide 35: Send and Receive
Remote Process
Process
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Complete
CQE
CQE
Fabric

## Slide 36: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
Fabric
Target Buffer

## Slide 37: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
WQE
Fabric
Target Buffer

## Slide 38: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
WQE
Remote Process
Process
Fabric
Data packet
Target Buffer
Read / Write

## Slide 39: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
Complete
CQE
Fabric
Target Buffer